## Slide 1: University of St. Thomas Graduate Programs in Software Internet of Things SEIS 744 IoT Final Project Weather Frame
By Basma Alboug

## Slide 2: The Weather frame IoT project
Every day before I leave home I check the weather on my phone to know what should I ware. Especially here in Minnesota the weather can drop or rise up to 10 degrees in the same day. So, I thought it would be nice to have a wall decor that provide the updated weather information
It Match the IoT concept
I wanted to use the stuff I bought

## Slide 3: How does it match the IoT concept
LCD blue shield
Moisture sensor grove
D1 Wifi UNO based ESP-8266
Arduino UNO
Wall USB charger
Object
Shadow box

## Slide 4: The parts
Shadow box
LCD
D1 wifi UNO
Breadboard
Arduino UNO
USB Port Power
Moisture Sensor
330k
Resistor
Jumper wires
LED

## Slide 10: How does it work
The Moisture sensor is connected to yellow and blue LED light
  If moisture sensor got wet it will flash the blue LED to show its raining otherwise the yellow LED will light to show that its clear sky
I connect the D1 UNO board to my home Wi-Fi network to download the weather data from the openweathermap.org website for my location. The data is updated every 10 minutes, then it will print on the LCD display
  I had to add my username and password for my home Wi-Fi network
  Add the API key from the openweathermap.org website
  Add the city ID from openweathermap.org website

## Slide 11: Pulling the weather data
Temperature
Pressure
Humidity

## Slide 12: The code
From the attached Arduino file

## Slide 13: The challenges
First, I had challenges with temperature sensor reading strange values, then I changed the idea to read the temperature from the cloud.
Finding the right library and Installing it was kind of challenge
It took me time to figure out why the LCD doesn’t show any characters and how to changing the LCD light brightness

## Slide 14: Future
I want to continue improving this project
I want to play with the design little bit, such as change the fame size make it smaller
I want add more features such as light sensor for showing day-night
I want use it at home hang it on the wall, to get updated about the weather outside

## Slide 15: Fritzing

## Slide 16: References
https://github.com/bblanchon/ArduinoJson
http
http://garagelab.com/page/tutorial-how-to-use-the-moisture-sensor-grove
https://openweathermap.org/
https://www.banggood.com/WeMos-D1-R2-WiFi-ESP8266-Development-Board-Compatible-Arduino-UNO-Program-By-Arduino-IDE-p-1011870.html?p=DQ30066511122014069J&utm_campaign=educ8stv&utm_content=huangwenjie
http://educ8s.tv/esp8266-weather-display/